## Slide 1: Cybersecurity and the Insider Threat Nuclear & Radiological Facilities
Risk Management Exercise
PNNL-SA-183134
Notes: Instructor Notes:
You may consider changing the dates on the slides starting on slide 10.
You can break the students up into groups, ask the questions and then debrief each decision slide as a whole class.
Each group selects a provided option or produces their own decision. Then they present their case to the class. Debate occurs.
Let the students answer the questions on each slide before continuing to the next.

## Slide 2: Confidentiality, Integrity, Availability (CIA Triad) Asset & Vulnerability Management
The Protection Goals of Cybersecurity
Confidentiality
Protection against access by unauthorised persons.
Confidentiality is guaranteed when objects defined as
worthy of protection (system, function, or datasets) are
only disclosed to authorised subjects (human, system or
function).
Integrity
Integrity is guaranteed when only authorised subjects
(human or system) correctly process an object (system,
function or dataset) for an authorised purpose. This
requires that the objects are specified and the processing
is traceable.
Availability Availability is ensured when the authorised subjects (human or system) have permanent access to the objects (system, function or databases) required to perform their tasks within the time jointly defined, as necessary. This presupposes that the necessary measures have been developed, implemented and practised for timely recovery or for safeguarding against disruptions.
Overview of
Exercise
Notes: Instructor Notes:
The whole point of the presentation is to lead the participant to understand that a structured and systematic approach to cyber security is not only needed but critical if they want to protect their nuclear and radiological assets.
While there are many methodologies and frameworks for building cybersecurity, this workshop will introduce the 5 core tenets of the NIST Cybersecurity Framework:
  Identify
  Detect
  Protect
  Respond
  Recover
All slides are led to lead the participant to this conclusion. Each attack described for adversary TTP leads to the need for one of these tenants.

## Slide 3: IDENTITY PROTECT DETECT RESPOND
Cyber Attack Continuum
Before attack
During attack
After attack
Identify | protect
detect
Respond | recover
Notes: Instructor Notes:
Highlight the continuum of a cyber attack.
We seek to identify potential attack points (vulnerabilities)
We seek to protect potential pathways into our environment
We put detection points in our environment to trigger response and recovery activities
Once detected we move into incident response mode with the goal of containing and remediating any issues
Finally, we recover the system to a trusted and reliable state.

## Slide 4: Building a Cybersecurity Assessment Team
NUREG 6847 Describes a CSAT Team of 3 to 7 Individuals with Broad Technical Knowledge in:
  ​Information and Digital System Technology Areas of cybersecurity, software development and application, computer system administration, and computer networking. In particular, knowledge is required of the digital systems involved in plant operations, including digital instrumentation and control systems, and those involved in plant business systems.
  Nuclear Power Plant Operations, Engineering and Safety Knowledge of overall facility operations and plant technical specifications. Staff representing this technical area must be able to trace the impact of a vulnerability or series of vulnerabilities in connected digital asset outward through plant subsystems and systems so that the overall impact on safety, security, and emergency preparedness of the plant can be evaluated.
  Physical and Operational Security Including in-depth knowledge of the plant’s physical and operational security program.
  Additional Considerations In addition to the above requirements, specialized in-depth cybersecurity skills are required to perform the electronic validation testing and optional scanning activities. The plant may not have on-site personnel trained and experienced in this arena. If this expertise is not available onsite, corporate-level cybersecurity personnel, an independent cybersecurity organization, or other sources of the validation expertise may be considered.
Overview of
Exercise
Notes: Instructor Notes:
This is a build up to the basis of the exercise. A cybersecurity assessment team will have a diverse set of skills across multiple people.

## Slide 5: Plant Emergency / Incident Response Team
Chief Executive Officer
Chief Financial Officer
Chief Security Officer
Human Resource Manager
Chief Operating Officer
Operations Manager
Engineering Manager
Maintenance Manager
Training Manager
Records Manager
Payroll and Benefits Manager
Regulatory Affairs Manager
Public Relations Manager
Physical Protection Manager
Cybersecurity Manager
IT Administration Manager
Administrative Support Manager
Procurement Manager
Generic Support Manager
Physical Protection of Plants and Materials
10 CFR Part 73
Physical Protection System
10 CFR 73.1(a)
On-Site Physical Protection Program and Security Organization
10 CFR 73.55(b)(1)
Cybersecurity Program
10 CFR 73.54(b)(2)
10 CFR 73.54(b)(3) “…incorporate the cybersecurity program as a component of the physical protection program…”
Notes: Instructor Notes:
Cybersecurity is a component of a broader nuclear security program.

## Slide 6: Tabletop: [IDENTIFY] Managing Risks Asset & Vulnerability Management
A nuclear power plant has recently named you as head of cybersecurity
You will be responsible for making strategic cybersecurity decisions for this power plant
A series of scenarios will be reviewed. presented requiring a decision and dealing with any residual risks and/or consequences.
Overview of
Exercise
Notes: Instructor Notes:
Scenario setup – Each small group is to act as if they collectively are the head of cyber security and make decisions as if they were in that role.

## Slide 7: Asset Management Asset & Vulnerability Management
Inventory
With an inventory, IT/OT systems are identified and
described in their interaction, for which appropriate
protective measures must be defined in a security
concept.
Assessment
When assessing the inventoried IT/OT systems, the need
for protection is determined from an IT security
perspective. The protection goals of IT security (C, I, A)
must be defined.
Prioritization
Prioritisation involves determining and prioritising the
necessary protection measures based on the defined
protection needs.
Mitigation
The defined protective measures shall be concretely
planned and implemented. The effectiveness of the
measures shall be reviewed at regular intervals.
Overview of
Exercise
Notes: Instructor Notes:
Identify – You cannot identify issues if you don’t know what systems you have. The first step is to create an inventory of all our assets. They you will assess those systems for their primary goal to establish protection strategies. Assets/systems are then prioritized, and mitigations applied in a graded approach.

## Slide 8: Scenario Setup Asset & Vulnerability Management
Initial situation:
- lack of responsibilities in the area of IT security
- Lack of basic information (inventory of IT systems, lack of protection needs assessment, lack of risk management, etc.).
Objectives:
- Assigning roles that are necessary for mastering the scenarios, this shows that in an emergency not only one person decides, but the decisions must always be made in consideration of the current situation. <<I really like this idea>>
- Protection needs assessment (CIA) of the existing IT assets
- Targeted trading based on the scenarios
Overview of
Exercise
Initial Situation:
Lack of responsibilities in the area of IT security
Lack of basic information (inventory of IT systems, lack of protection needs assessment, lack of risk management, etc.).
Objectives:
Assigning roles that are necessary for mastering the scenarios, this shows that in an emergency not only one person decides, but the decisions must always be made in consideration of the current situation.
Protection needs assessment (CIA) of the existing IT assets
Targeted trading based on the scenarios
Notes: Instructor Notes:
Establish the culture of the plant which is focused on barely meeting licensing requirements to maximize profits. Corner cutting that saves money without violating the ability to operate is generally ignored.

## Slide 9: [IDENTIFY] Building Blocks Building a Risk Management Process
People
Process
Tech
What are the inputs into a risk management system?
What are the types of assets we should examine?
System & Assets
Vulnerable?
Exploitable?
Risk Exists
No Risk
NO
NO
YES
Risk Management Process
YES
What are the inputs into a risk management system?
What are the types of assets we should examine?
Notes: Instructor Notes:
Key Objective:
In this exercise we are going to look at a facility who has decided to start building a cybersecurity program.
This first step is building a Cybersecurity Assessment team. You guys are in charge.
In this exercise, we are going to look at identifying the critical digital assets at the facility.
The goal of this exercise is understanding why identifying and prioritizing assets is so crucial and important.

## Slide 10: Scenario: Decisions June 17, 2018
What are the core functions of a risk management program?
Who should be involved in developing the program?
The plant director has issued an order for you to establish a cyber risk management program at Seaside.
What are the data needs to establish a risk management program?
What type of personnel is needed to accomplish this task?
To expedite the process, is hiring outside contractors appropriate?
What systems at the plant should your staff prioritize to complete the quickest?
How will you ensure the data is accurate?
What type of data about the assets should be accumulated?
“While cybersecurity is important, you must operate within a budget. As such, I need you to evaluate the cyber risks, prioritize, and make decisions that are fiscally responsible.” - Mardil Voron
Notes: Instructor Notes:
Share the following story with the class:
Your boss has asked you to establish a cybersecurity program.
You won’t have an unlimited budget. As a result, we need to understand our risks so we can prioritize our actions.
Instructions for class.
Review the questions.
Ask the students to answer the 6 questions through Mentimeter. Please note: If trainees are not able to access Mentimeter, then administer the questions through a class discussion. Start by dividing the trainees into groups. Ask trainees to discuss the questions within their group. Ask for a representative from each group to share their answers to the questions with the larger group when the larger group reconvenes.
One thing to highlight on the people, process, and tech front = Which departments have hired outside contractors to help them accomplish their goals. While the cybersecurity division may hire outside help, it is likely that outside help has been hired by other departments .

## Slide 11: Introduction to Facility Network Configuration
Are there any vulnerabilities in the diagram?
Is the network segmented or flat?
External
Internet
Remote Users
Remote Vendors
Internet Facing
DMZ – Sanitizing Area
Internet
Email Server
Web Server
Firewall
Business Network
Corporate Systems
Business Servers
Enterprise Computers
Engineering Network
Management Systems
Application Servers
Domain Controllers
Historian
Engineering Network
Operational Systems
Field Workstation(s)
Firewall
Safety Analog Devices
Engineering Workstations
Safety Parameter Display System
PLC
Field Input/Output Devices
Balance of Plant Digital Devices
Physical Security Systems
Database Server
Notes: Instructor Notes:
Review the network diagram with the students.
  A digital inventory was taken 3 years ago. Any configuration changes that have been made are not physically noted in the documentation
  The key thing to bring up is that there are basically 2 networks at the facility: business and engineering.
  There is a demilitarized zone (DMZ) between the outside and the business network.
  There is a firewall separating the business network and the engineering network.
  There are no engineering systems allowed to have direct access to the internet.
Be sure to state that the safety systems are analog.
Tried to set this up like a bus network, however it was challenging in PowerPoint.

## Slide 12: Introduction to Facility Engineering Network / Management Systems
Are there any vulnerabilities in the diagram?
Is the network segmented or flat?
Digital Controls
Digital SPDS
Field Input/Output Devices
Analog Displays and
Controls
HMI
Operational I&C
Safety I&C
Field
Workstations
Safety Analog
Devices
PLC
Balance of Plant Digital Devices
Plant Equipment
PLC
Field
Workstations
Plant
Network
Plant
Network
Notes: Instructor Notes:
Review the network diagram with the students.
  A digital inventory was taken 3 years ago. Any configuration changes that have been made are not physically noted in the documentation
  The key thing to bring up is that there are basically 2 networks at the facility: business and engineering.
  There is a demilitarized zone (DMZ) between the outside and the business network.
  There is a firewall separating the business network and the engineering network.
  There are no engineering systems allowed to have direct access to the internet.
Be sure to state that the safety systems are analog.
Tried to set this up like a bus network, however it was challenging in PowerPoint.

## Slide 13: Prioritization is Key August 1, 2018
Be sure to reference the presentation materials
What are the core systems of a nuclear power plant?
Categorize each of the 10 systems into either High, Medium or Low Priority.
Access Control System for the Vital Area at the nuclear facility.
Reactor Protection System
Accounts Payable Enterprise System
Turbine Operator Station
Historian on the enterprise network
Engineering / Database Developer Server
Safety Systems
Redundant Historians on Engineering Network
Video Management System of limited area
Radio Communications for Guard Force
Then, assign a CIA security goal to the items categorized as High or Medium Priority.
Your deputy has requested assistance in prioritizing systems. You both decide to prioritize the systems based on the consequences if the system fails.
You are allowed:
  2 - High Priority Systems
  5 - Medium Priority Systems
  3 - Low Priority Systems
NAME: Tom Bombadil
ORGANIZATION: Seaside NUCLEAR
POWER PLANT
RESPONSIBILITIES: CYBERSECURITY & INCIDENT RESPONSE
SPECIALTY: NETWORK ARCHITECTURE
Notes: Instructor Notes:
Have the students prioritize which systems are the most crucial or have the most consequence if they failed and have them explain why.
What’s the CIA value?
This is set up as a Mentimeter activity. Have participants do the activity through Menitmeter or small group discussion.
Please note: If trainees are not able to access Mentimeter, then administer the questions through a discussion. Start by dividing the trainees into groups. Ask participants to discuss the questions within their group. Ask for a representative from each group to share their answers to the questions with the larger group when the larger group reconvenes.

## Slide 14: Scenario Update #4: Accounts Payable is Down January 26, 2019 [SATURDAY] @ 1715
Are we safe?
What information do we need? Is this a cyber incident?
“Cybersecurity is also about ensuring operational reliability! Get our Accounts Payable servers back into operation ASAP. These servers are bringing in the money and thus there are bringing on your income!” - Mardil Voron
Time Stamp on Events
Time | Description
0900 | Several users working over the weekend have called technical support stating that the network is slow.
1330 | The Accounts Payable servers that were being upgraded are “timing out” due to little to no bandwidth to complete normal tasks.
Notes: Instructor Notes:
Walk them through the scenario.
09:00 – Tech support is reporting that they have received a ton of calls for a Saturday saying that the network or individual computers are operating really slowly. Next several hours – call frequency of problems increases with all reporting the same issue.
1330 – The new server that was being updated failed and crashed. None of the accounts payable division can reach their data on the server.
We don’t know enough to make the call whether the plant is safe or not. We need more data.

## Slide 15: Scenario Update #2: An Urgent Matter December 14, 2018
What is a worm?
What systems are affected?
What are should your first steps be in response?
Sapphire Computer Worm – AKA “Sapphire” – exploits vulnerabilities in Microsoft SQL Servers.
It has little impact of home or desktop PCs.
It does not infect Linux, Mac, or Unix
What does SAPPHIRE do?
Once the server is infected, it endeavors to spread quickly by sending a similar payload to arbitrary IP addresses on the host network.
This brings on a denial-of-service condition on its targets.
Mitigations Options
Long-Term
  Microsoft has created patch that can be installed
Short-Term
  Block SAPPHIRE signature at the firewall.
  Since the worm does not taint any files, an infected machine can be cleaned by just rebooting the machine to a previous configuration.
  However, it can get re-contaminated if connected with another infected system.
WARNING!!! WARNING!!!
MALWARE NAME: SAPPHIRE
MALWARE TYPE: WORM
IMPACT: DENIAL OF SERVICE
SYSTEMS VULNERABLE: ALL WINDOWS SQL SERVERS
Notes: Instructor Notes:
Have the students prioritize which systems are the most crucial or have the most consequence if they failed and have them explain why.
What’s the CIA value?
Write this out on a whiteboard if possible.

## Slide 16: Options Analysis December 14, 2018
With limited resources, how will you prioritize your action?
Which option is the best decision for Seaside?
Prioritizing Actions
Option 1
Option 2
Option 3
[ACTION] – Pull all cyber personnel off current duties and begin testing and deployment of Microsoft Patch
[PRO] Quickest option to securing against SAPPHIRE
[CON] Delay of Inventory
[ACTION] – Block SAPPHIRE at the firewall between external and corporate network
[PRO] Quickest way to prevent SAPPHIRE from getting into Seaside. Cyber staff continues Inventory
[CON] All systems still vulnerable to SAPPHIRE
[ACTION] – Hybrid of options 1 and 2. Requires identifying prioritized systems
[PRO] Begins immediate defense against SAPPHIRE and continues inventory process.
[CON] Some delay in inventory
Option 4
[ACTION] – Participant Defined
[PRO] – Participant Defined
[CON] – Participant Defined
Notes: Instructor Notes:
It is fine if students want to come up with a 4th option.
The main thing is we need them to understand that any decision to do anything has pros and cons and impacts staff/personnel on the cyber team.
This is set up as a Mentimeter activity. Have participants do the activity through Menitmeter or small group discussion.
Please note: If trainees are not able to access Mentimeter, then administer the questions through a discussion. Start by dividing the trainees into groups. Ask participants to discuss the questions within their group. Ask for a representative from each group to share their answers to the questions with the larger group when the larger group reconvenes.

## Slide 17: Scenario Update #3: Rogue Data Flows January 4, 2019
What should be done with this T1 connection?
Is this a violation of the network policy?
External
Internet
Remote Users
Remote Vendors
Internet Facing
DMZ – Sanitizing Area
Internet
Email Server
Web Server
Firewall
Business Network
Corporate Systems
Business Servers
Enterprise Computers
Engineering Network
Management Systems
Application Servers
Domain Controllers
Historian
Engineering Network
Operational Systems
Field Workstation(s)
Firewall
Safety Analog Systems
Engineering Workstations
Safety Parameter Display System
Programmable Logic Controller
Field Input/Output Devices
Digital Devices
Notes: Instructor Notes:
Based on whatever option they chose, tell participants that the team is implementing their orders.
Meanwhile, Initial inventory analysis has identified a rogue T1 connection bridging a vendor working remotely to the business network. The purpose of the connection is to enable the vendor to work remotely on the corporate systems for a vital upgrade for the accounts payable division. The business entities at the plant state that this connection is important to their mission.
What should be done about this rogue connection? Formalize it and establish it as an authorized conduit or kill it?
What are the risks?

## Slide 18: Options Analysis January 4, 2019
Is there a legitimate business need for the connection?
Which option is the best decision for Seaside?
Prioritizing Actions
Option 1
Option 2
Option 3
[ACTION] – Redirect vendor’s connection back through firewall
[PRO] Restores policy compliance
[CON] Negative impact to accounts payable and will delay new system implementation by months
[ACTION] – Permit the connection during upgrades.
[PRO] Does not impact business operations
[CON] Bypass of firewall continues.
[ACTION] – Permit the connection during upgrades but work with vendor to establish cyber rules
[PRO]No impact to business operations
[CON] Small delay in inventory activities
Option 4
[[ACTION] – Participant Defined
[PRO] – Participant Defined
[CON] – Participant Defined
Notes: Instructor Notes:
It is fine if students want to come up with a 4th option.
The main thing is we need them to understand that any decision to do anything has pros and cons and impacts staff/personnel on the cyber team.
This is set up as a Mentimeter activity. Have participants do the activity through Menitmeter.
Please note: If trainees are not able to access Mentimeter, then administer the questions through small group discussion. Start by dividing the trainees into groups. Ask participants to discuss the questions within their group. Ask for a representative from each group to share their answers to the questions with the larger group when the larger group reconvenes.

## Slide 19: Scenario Update #4: SPDS is Down January 26, 2019 [SATURDAY] @ 1715
Are we safe?
What information do we need? Is this a cyber incident?
Time Stamps on Events
Time | Description
1500 | Users on the engineering network report their workstations are taking a long time to pull up data.
1600 | Control Room Operators notice sluggish data from various systems.
1650 | The Safety Parameter Display System (SPDS) – the plant’s digital HMI for safety – has crashed.
1713 | The Plant Process Computer (PPC) crashed.
“What is happening?!? I thought cybersecurity programs were supposed to protect us from this stuff. Is this a cyber event or a maintenance issue? Bottom line, I need to know, is the plant safe? You have 10 minutes to tell me.”
- Mardil Voron
Notes: Instructor Notes:
Walk participants through the scenario.
1500 – Issues are now spreading from the business network to the engineering network.
1600 – Control Room operators see their numbers coming in slow.
1650 – Safety Parameter Display System (SPDS) Crashes.
1713 – Plant Process Computer (PPC) crashes.
We don’t know enough to make the call whether the plant is safe or not. We need more data.

## Slide 20: Scenario Update #4: Are we Safe? January 26, 2019 [SATURDAY] @ 1717
What is happening?
How is the malware moving from the business network to the engineering network?
External
Internet
Remote Users
Remote Vendors
Internet Facing
DMZ – Sanitizing Area
Internet
Email Server
Web Server
Firewall
Business Network
Corporate Systems
Business Servers
Enterprise Computers
Engineering Network
Management Systems
Application Servers
Domain Controllers
Historian
Engineering Network
Operational Systems
Field Workstation(s)
Firewall
Safety Analog System
Engineering Workstations
Safety Parameter Display System
Programmable Logic Controller
Field Input/Output Devices
Digital Devices
WARNING!!! WARNING!!!
MALWARE NAME: SAPPHIRE
MALWARE TYPE: WORM
IMPACT: DENIAL OF SERVICE
SYSTEMS VULNERABLE: ALL WINDOWS SQL SERVERS
Notes: Instructor Notes:
If the students chose option 1 to disconnect the T1, tell them that you gave the order, but no one implemented your order [true to life]. Also, the malware spread because the Firewall in the Corporate demilitarized zone (DMZ) had a ruleset for SAPPHIRE. We didn’t set that same rule for the firewall between corporate and business because it wasn’t connected to the internet. No one thought it would happen.
Is the plant safe? The answer should be: we as cyber individuals don’t know enough to make that call. Further, it probably isn’t our call. Who should we speak to get more data?

## Slide 21: Scenario Update #4: Are we Safe? January 26, 2019 [SATURDAY] @ 1720
What type of data do you need to understand whether the plant is safe?
What is the SPDS saying?
SAFETY PARAMETERS DISPLAY SYSTEM (SPDS)
Reactor Control System (RCS)
STEAM
GENERATOR
A
STEAM
GENERATOR
B
STEAM
GENERATOR
C
HEAD
TEMPERATURE
####
HOT LOOP A
HOT LOOP B
COLD LOOP B
COLD LOOP A
####
####
####
####
HOT LOOP C
####
COLD LOOP c
####
###%%
###%%
REACTOR VESSEL LEVEL
RCS / UPPER HEAD
SATURATION MARGINE
PLENUM
OVERVIEW SCREEN
CORE
RCS PRESSURE
####
ALARM LIST
CORE
SUM
CORE
MAP
RCS
SUM
SYS
SUM
SHOW
LEGEND
PRINT
SCREEN
DIRECTORY
NAME: Raina Galadriel
ORGANIZATION: Seaside NUCLEAR
POWER PLANT
RESPONSIBILITIES: CONTROL ROOM SUPERVISOR
SPECIALTY: NUCLEAR ENGINEERING
“Are we safe? Well, it depends on how you look at this event. Digitally, we have no idea what is going on inside the core. Thankfully, our analog system was never uninstalled. Per the analog system, we are fine.”
- Raina Galadriel
Notes: Instructor Notes:
Participants are asked the following 4 questions in the upcoming slides through class discussion or Mentimeter:
  What type of data is communicated by the SPDS?
  Is this important information?
  Is this a critical system?
  What is it’s CIA Triad value?
Everything is timing on data entry. As a result, we are only getting ### in place of requisite data. Per Raina, the analog system is still up.
Which system numbers do you think are trustworthy?
Please note: If trainees are not able to access Mentimeter, then administer the questions through a discussion. Start by dividing the trainees into groups. Ask participants to discuss the questions within their group. Ask for a representative from each group to share their answers to the questions with the larger group when the larger group reconvenes.

## Slide 22: Scenario Update #4: Are We Safe? January 26, 2019 [SATURDAY] @ 1723
Which system should we trust for our safety data?
Is this system safe or should we SCRAM?
PLENUM
CORE
REACTOR HEAD
SAFETY DATA
ANALOG
SYSTEM
CONTROL
ROOM
SAFETY DISPLAY PARAMETERS SYSTEM
TRICONEX CHANEL 1
Maintenance Station
CONTROL
ROOM
SAFETY DISPLAY PARAMETERS SYSTEM
ANALOG
FIBER OPTIC
X
X
Notes: Instructor Notes:
The old analog system shows all is functioning normally.
The digital system is not returning any information.

## Slide 23: Options Analysis January 26, 2019 [SATURDAY] @ 1723
Is the plant safe?
Who do we rely on for this type of information?
Is this a cyber decision?
Prioritizing Actions
Option 1
Option 2
Option 3
[ACTION] - Trust digital data. Plant is not safe. Hit the SCRAM button and begin emergency procedures.
[PRO] - Ensures plant safety.
[CON] - Negative impacts from publicity, governance, money, and operations.
[ACTION] - Trust analog data. Plant is safe. Digital system is down but analog is up.
[PRO] - Keeps plant running.
[CON] - If analog data is wrong, plant could be in serious trouble.
[ACTION] - Don’t know what to trust. Need more time to figure out solution. Work with Raina to determine safety assurance.
[PRO] - Find data that you can trust to make a decision.
[CON] - Time
Option 4
[ACTION] – Participant Defined
[PRO] – Participant Defined
[CON] – Participant Defined
Notes: Instructor Notes:
It is fine if students want to come up with a 4th option.
The main thing is we need them to understand this wouldn’t really be the cyber team's call. But here is a cyber issue that is causing safety to be questioned.
This is set up as a Mentimeter activity. Have participants do the activity through Menitmeter.
Please note: If trainees are not able to access Mentimeter, then administer the questions through a discussion. Start by dividing the trainees into groups. Ask participants to discuss the questions within their group. Ask for a representative from each group to share their answers to the questions with the larger group when the larger group reconvenes.

## Slide 24: IDENTITY PROTECT DETECT RESPOND How did our system work?
What could we have done differently on the protection side?
Detection and Response?
Cyber Attack Continuum
Before attack
During attack
After attack
Identify | protect
detect
Respond | recover
What can we learn?
What can we learn?
Did protection measures protect the CIA security goal?
Where did it fail in Seaside?
What can we learn?
How was the attack detected?
Was detection timely?
Was detection coordinated with protection?
What can we learn?
Did response eradicate adversary?
Did response restore critical functions?
What can we learn?
Notes: Instructor Notes:
What happened between 09:00 a.m. and 4:00 p.m. The issue is that the slow network which was an Indicator of Compromise (IOC) for SAPPHIRE sat with computer support thinking it was a network issue. What can we do on the detection side to speed up analysis between 09:00 a.m. and 4:00 p.m.?

## Slide 25: Video Asset & Vulnerability Management
Seaside Nuclear Power Plant
https://vimeo.com/639223567
Notes: Instructor Notes:
INSIDER CATEGORIES
https://vimeo.com/639223567
Password: pT'!u~9V
Seaside Nuclear Power Plant (Davis-Besse Incident): Starts at 10:17

## Slide 26: Lessons Learned June 17, 2018
What are the core functions of a risk management program?
Who should be involved in developing the program?
What is the insider impact?
What is impacted?
  Business Continuity (Organization survivability)
  Worldwide Implication
  Safety
How could these incidents have been prevented?
  Organizational measures
  Technical measures
What was missing in the organization?
  Lack of policy
  Lack of awareness
  Lack of technical measures
Timeline Discussion:
  Examples (NotPetya, Fukishima, etc.)
“While cybersecurity is important, you must operate within a budget. As such, I need you to evaluate the cyber risks, prioritize, and make decisions that are fiscally responsible.”
- Mardil Voron
Notes: Instructor Notes:
There are two options to run this exercise.
Small group discussion and/or
Mentimeter (or equivalent)
Instructions for class:
Have students review the questions through Mentimeter. Please note: If trainees are not able to access Mentimeter, then administer the questions through small group discussion. Start by dividing the trainees into groups. Ask participants to discuss the questions within their group. Ask for a representative from each group to share their answers to the questions with the larger group when the larger group reconvenes.

## Slide 27: Davis Besse & Slammer January 25, 2003 [SATURDAY]
What really happened?
What can we learn from this attack in a real-world environment?
01
02
03
04
05
Identify
Governance
Asset Management
Risk Assessment
Risk Management
Protect
Access Control
Awareness
Data Security
Processes
Technology
Detect
Security Events
Digital Monitoring
Detection Process
Response
Planning
Communications
Analysis
Mitigations
Improve
Recover
Planning
Improvements
Communications
You note in your cover letter that the Davis-Besse plant was “in a safely defueled condition” at the time of infection. This is not reassuring.
What would be the safety consequences of Slammer had the plant been fueled an operational?
What impact would the infection have had on the ability to respond to any problems?
How will you ensure that the plants enforce orders as directed?
Notes: Instructor Notes:
Walk them through the real deal.
Walk them through slammer scenario similar to Davis Besse except for Seaside.
<! - - Source Data -->
The breach did not pose a safety hazard. The troubled plant had been offline since February 2002, when workers discovered a 6-by-5-inch hole in the plant's reactor head. Moreover, the monitoring system, called a Safety Parameter Display System, had a redundant analog backup that was unaffected by the worm. But at least one expert says the case illustrates a growing cybersecurity problem in the nuclear power industry, where interconnection between plant and corporate networks is becoming more common and is permitted by federal safety regulations. The Davis-Besse plant is operated by FirstEnergy Corp., the Ohio utility company that's become the focus of an investigation into the northeastern U.S. blackout last week. The incident at the plant is described in an April e-mail to the Nuclear Regulatory Commission (NRC) from FirstEnergy, and in a similarly-worded March safety advisory distributed privately throughout the industry over the "Nuclear Network," an information-sharing program run by the Institute of Nuclear Power Operations. The March advisory was issued to "alert the industry to consequences of Internet Worms and Viruses on Plant Computer Systems," according to the text. The reports paint a sobering picture of cybersecurity at FirstEnergy. The Slammer worm entered the Davis-Besse plant through a circuitous route. It began by penetrating the unsecured network of an unnamed Davis-Besse contractor, then squirmed through a T1 line bridging that network and Davis-Besse's corporate network. The T1 line, investigators later found, was one of multiple ingresses into Davis-Besse's business network that completely bypassed the plant's firewall, which was programmed to block the port Slammer used to spread. "This is in essence a backdoor from the Internet to the Corporate internal network that was not monitored by Corporate personnel," reads the April NRC filing by FirstEnergy's Dale Wuokko. "[S]ome people in Corporate's Network Services department were aware of this T1 connection and some were not." Users noticed slow performance on Davis-Besse's business network at 9:00 a.m., Saturday, January 25th, at the same time Slammer began hitting networks around the world. From the business network, the worm spread to the plant network, where it found purchase in at least one unpatched Windows server. According to the reports, plant computer engineers hadn't installed the patch for the MS-SQL vulnerability that Slammer exploited. In fact, they didn't know there was a patch, which Microsoft released six months before Slammer struck. Operators Burdened By 4:00 p.m., power plant workers noticed a slowdown on the plant network. At 4:50 p.m., the congestion created by the worm's scanning crashed the plant's computerized display panel, called the Safety Parameter Display System. An SPDS monitors the most crucial safety indicators at a plant, like coolant systems, core temperature sensors, and external radiation sensors. Many of those continue to require careful monitoring even while a plant is offline, says one expert. An SPDS outage lasting eight hours or more requires that the NRC be notified. At 5:13 p.m., another, less critical, monitoring system called the "Plant Process Computer" crashed. Both systems had redundant analog backups that were unaffected by the worm, but, "The unavailability of the SPDS and the PPC was burdensome on the operators," notes the March advisory. It took four hours and fifty minutes to restore the SPDS, six hours and nine minutes to get the PPC working again. FirstEnergy declined to elaborate on the incident. The company has become the focus of an investigation into last week's northeastern U.S. blackout. Though the full cause of the blackout has yet to be determined, investigators have reportedly found that it began when an Ohio high-voltage transmission line "tripped" after sagging into a tree. An alarm system that was part of FirstEnergy's Energy Management System failed to warn operators at the company's control center that the line had failed. Asked if last week's "Blaster" worm might have had a hand in the alarm system failure, just as Slammer disabled the Davis-Besse safety display panel, FirstEnergy spokesman Todd Schneider said, "We're investigating everything right now." "I have not heard of anything like that," added Schneider. "The alarm system was the only system that was not functioning." SCADA Issues The Davis-Besse incident was not Slammer's only point of impact on the electric industry. According to a document released by the North American Electric Reliability Council in June, Slammer downed one utility's critical SCADA network after moving from a corporate network, through a remote computer to a VPN connection to the control center LAN. A SCADA (Supervisory Control and Data Acquisition) system consists of central host that monitors and controls smaller Remote Terminal Units (RTUs) sprinkled throughout a plant, or in the field at key points in an electrical distribution network. The RTUs, in turn, directly monitor and control various pieces of equipment. In a second case reported in the same document, a power company's SCADA traffic was blocked because it relied on bandwidth leased from a telecommunications company that fell prey to the worm. Reports on the effect of last week's Blaster worm on the electric grid, if any, have yet to emerge. The Slammer attacks came after years of warnings about the vulnerability of power plants and electric distribution systems to cyber attack. A 1997 report by the Clinton White House's National Security Telecommunications Advisory Committee, which conducted a six-month investigation of power grid cybersecurity, described a national system controlled by Byzantine networks riddled with basic security holes, including widespread use of unsecured SCADA systems, and ample connections between control centers and utility company business networks. "[T]he distinct trend within the industry is to link the systems to access control center data necessary for business purposes," reads the report. "One utility interviewed considered the business value of access to the data within the control center worth the risk of open connections between the control center and the corporate network." Future Safety Concerns An energy sector cybersecurity expert who's reviewed nuclear plant networks, speaking on condition of anonymity, said the trend of linking operations networks with corporate LANs continues unabated within the nuclear energy industry, because of the economic benefits of giving engineers easy access to plant data. An increase in plant efficient of a couple percentage points "can translate to millions upon millions of dollars per year," says the expert. He says Slammer's effect on Davis-Besse highlights the dangers of such interconnectivity. Currently, U.S. nuclear plants generally have digital systems monitoring critical plant operations, but not controlling them, said the expert. But if an intruder could tamper with monitoring systems like Davis-Besse's SPDS, which operators are accustomed to trusting, that could increase the risk of an accident. Moreover, the industry is moving in the direction of installing digital controls that would allow for remote operation of plant functions, perhaps within a few years, if the NRC approves it. "This is absolutely unacceptable without drastic changes to plant computer networks," says the expert. "If a non-intelligent worm can get in, imagine what an intruder can do." Jim Davis, director of operations at the Nuclear Energy Institute, an industry association, says those concerns are overblown. "If you break all the connections and allow no data to pass from anywhere to anywhere, you've got great security -- but why'd you put the digital systems in the first place?," says Davis. Davis says the industry learned from the Davis-Besse incident, but that the breach didn't prove that connections between plant and corporate networks can't be implemented securely. "You can put a well-protected read-only capability on a data stream that provides you reasonable assurance that nobody can come back down that line to the control system," says Davis. Last year the NEI formed a task force to develop updated cybersecurity management guidelines for the industry. The results -- which will be secret -- are expected within a few months. As part of a research effort earlier this year, the NEI's task force worked with the NRC and a contractor to review cybersecurity at four nuclear power plants. The details of the review are classified as "Safeguards" material, but Davis says the investigation found no serious problems. "There are no issues that generate a public health and safety concern," says Davis. "Sometime people get very anxious about digital systems and what you could or couldn't do with digital systems, but in lots of cases you've got switches and valves and little override buttons on this thing and that thing that could cause a component to shut down as quickly as any digital system," Davis says. Despite the Slammer breach, FirstEnergy was apparently not in violation of NRC's limited, and aging, cybersecurity regulations. For its part, the commission wouldn't comment on the incident. The NRC has faced fierce criticism for not acting sooner to curb far more serious physical safety problems at the plant.

## Slide 28: Introduction to Facility Seaside Industrial Solutions
Does culture at a facility impact security?
What does this plant’s culture tell you?
Seaside Power Plant 1
Pressurized Water Reactor
History of Safety Issues
Boric Acid Leakage / Reactor Vessel Degradation
Notes: Instructor Notes:
This slide is optional. Use it if you want to have a discussion on nuclear security culture and how culture can impact all aspects of security. If not hide or delete the slide.
Review the bullets below with the students to give them a history of the facility.
Ask the questions in the top right section to have the students make an evaluation the facilities’ culture for compliance?
  Seaside Industrial Solutions is a multi-national radiological / nuclear provider. Their revenue streams range from energy production to building radiological equipment for industrial purposes.
  Earlier this year at one of their nuclear power plants, a cavity was discovered in the reactor pressure vessel head adjacent to a control rod drive mechanism (CRDM) nozzle penetration.
  Corrosion caused by boric acid leakage from the CRDM nozzle cracks.
  Cavity extended through the base metal of the vessel head to the 3/8” stainless steel cladding on the inside of the head.
  Stainless steel cladding was not designed to maintain reactor coolant pressure boundary.
  During an inspection by the competent authority, Seaside leadership was scolded for not taking a proactive approach to this problem.
  Despite the reprimand, the competent authority agreed that performance indicators at the plant were “green” meaning the corrosion did not impact safety or the operability of the plant.
  However, it is felt by personnel throughout the plant that making suggestions to leadership that increase cost are discouraged.
  There is a culture of complacency and lack configuration control.

## Slide 29: Discussion
Notes: Instructor Notes:
Have a round table discussion with participants Ask participants to share their feedback on the following questions:
  What suggestions do you have for improving any specific lesson?
  Was anything missing from the lesson content that would have improved the learning experience?
  What parts of the training benefited you the most, and why?